## Slide 1: Lance Armstrong said “It is not about the bike”
And that is because it was not about the bike – it was about the EPO etc. - Lance was on the juice……bad Lance and Floyd and Tyler and George….but all clean now !!
Today’s objective is to show you how to fit your mountain bike and road bike properly for maximum performance and pleasure with an emphasis on seat height…………….

## Slide 2
Scrolling text repeating until end of slide
So today’s objective is to show you how to fit your mountain bike and road bike properly for maximum performance and pleasure….and get ready for…

## Slide 3: Oct 9-16 Cycling - Union Cycliste Internationale UCI Road World Championships Doha, Qatar
And also there is the Tour De France July 2 – 24th

## Slide 4
Scrolling text repeating until end of slide
You will learn how to fit your mountain bike and road bike properly for maximum performance and pleasure with an emphasis on seat height…………….you will complete a self assessment about bike fitting, we will have a hands on experience and adjust the seat height, and some of you might go for a trial run. There will also be a takeaway handout on “Fitting Your Bike”……success will be evidenced by self assessment, discussion and hands on learning.
Lesson Objective – Fitting Your Bike

## Slide 5: Lesson Plan
Types of bikes - video
https://www.rei.com/learn/expert-advice/bicycle.html
Self Assessment – Bike Knowledge – What Do You Know?
Discussion of fitting your bike
Hands on Seat Adjustment
Trial Run
Fitting your bike – Handout
Summary

## Slide 6
How Bikes are Sized
Different types of bikes are sized differently and will have slightly different fits: Road bikes can come in both standard (S, M, L) sizes and numerical sizes. The same size across different brands can fit very differently and the number may not correlate to a common measurement. You might ride a size 54 Cannondale road bike, but a size 54 Giant road bike may feel quite different. Mountain bikes come in standard sizes (S, M, L) and are generally similar across brands. For example, if you like your size small GHOST mountain bike, it’s likely (but not definite), that you’ll want a small in other brands as well. Hybrid bikes, unsurprisingly, are a mix of the two, with more forgiving sizing than elite road bikes, but not quite as flexible as the sizing of most mountain bikes.

## Slide 7
Bike Frame Standover Height
First, make sure you can straddle your bike with your feet flat on the floor. Be sure to wear your cycling shoes when evaluating standover height, since they add to your overall leg length.
Road bikes: If the bike has a traditional straight top tube that is parallel to the ground,
you should have approximately 1" of clearance between the ground and tires when you lift the bike as
you’re straddling it.
If the bike has a sloping top tube (semi-compact or compact design) expect to have clearance of 2" or more.
Both men’s and women’s bikes can have compact frames.
Mountain bikes: When you lift the bike, you want 2" minimum clearance between the tires and the ground.
If your bike has full suspension, it’s okay to have less initial clearance (1"–2") because the suspension compresses
under your weight once you sit on the bike. That said, the amount of clearance is largely affected by the slope of
the top tube down toward the rear wheel. For example, if the slope is dramatic, you'll likely have ample clearance
no matter what size the frame is. Because of this, you can't rely solely on standover clearance to determine
if a bike fits.
Hybrid bikes: If your hybrid bike is a city commuter, use the road bike guidelines. If it’s a beach cruiser or
a step-through style, you don’t really have to worry about standover height.
Most of these have steeply sloping top tubes that let you step over easily and put your feet flat on the ground
when seated.

## Slide 9
General Bike Sizing Tips
While there are some basic fit considerations for any bike you’ll buy, bike sizing can become quite intricate if you are a serious rider looking for specific performance characteristics. This article focuses on entry-level fit considerations.
Your bike should fit how you currently ride. You may aspire to match that low, long, aerodynamic position of the pros, but it’s important to set the bike up to match your current abilities. As you work on strength, flexibility and endurance, you can readjust your fit later.
Fine-tuning the fit. First, identify your overall bike frame size. If you don’t have the right frame from the outset, you’ll have difficulty getting it comfortable no matter what adjustments you make later. Some adjustments can be made easily with the bike’s existing components (seat height, angle, etc.) and some may require swapping out a component (e.g., a new stem can change the location of the handlebars for a more comfortable riding position).

## Slide 10
Bike Seat (Saddle) Height
With your seat height and position dialed in, you have the best chance of pedaling efficiently and powerfully using your major leg muscles.
To check your seat position, ask a friend to hold the bike upright while you hop on the saddle.
Proper position:

## Slide 11
Proper position: With your foot at the bottom of the pedal stroke, you should see a slight bend in the leg, reaching about 80-90 percent of full leg extension. This is true for road, mountain and hybrid bikes. (If you expect to progress quickly on your mountain bike, you may also want to look for bikes with height-adjustable seatposts. These bikes let you raise or lower the seat by pushing a button, helping you adjust instantly to changing terrain.)

## Slide 12
Handout - Other Adjustments that you need to make………

## Slide 13
Adjusting the fore/aft position: Make adjustments by loosening the saddle binder bolt (sometimes called the seat fixing bolt) and sliding the saddle forward or backward as needed. This generally applies to road, mountain and hybrid bikes, but remember, this is just a starting point. As you become more experienced you may find you like to position your saddle a little differently.
Now check your saddle tilt. With few exceptions, the saddle should be parallel to the ground. To make saddle tilt adjustments, simply loosen the saddle binder bolt (or bolts) at the top of your seatpost (directly underneath your saddle) and adjust as needed.
(Note: The saddle binder bolt is different from the seatpost binder bolt.) Retighten the saddle bolt(s) before riding.

## Slide 14: Other Fittings
Fitting Women’s Bikes
Women often have proportionately narrower shoulders and longer legs compared to their torsos than men, and women-specific bikes are designed to meet these needs. Women’s bikes often have narrower handlebars and shorter or more compact frame dimensions. Some women find that men’s bikes fit well and are comfortable, but women-specific bikes may provide a more precise fit for some.
Fitting Kids’ Bikes
If you’re buying a bike for a beginning rider, it’s easy to want one they’ll “grow into,” but it’s especially important to buy a bike that fits well so they can ride comfortably and confidently while they learn.
Standover height: As with adult bikes, first check the standover height. Whatever the top-tube style, look for about 2"–4" of clearance.
Seat height: Most kids’ bikes are designed so they ride in a more upright position. They should be able to sit comfortably, see around them easily and grip the handlebars with a slight bend in their elbows. Their legs should be slightly bent at the bottom of the pedal stroke.

## Slide 15
We discussed the different types of bikes, did a self assessment, review of fitting, hands on adjustment of the seat, and for the brave – a trial ride…
A bike that fits well and is right for your height, flexibility and riding style is a bike you’ll love riding. A bike that fits poorly can lead to inefficient riding, muscle aches and pains, and general discomfort that might discourage you from riding as long or as far as you want.
https://www.rei.com/learn/expert-advice/bike-fit.html
Summary